## Slide 1
microServiceBus.com
tutorial
Mikael Hakansson
mikael.hakansson@axians.com
Aleyois Boix Chova
aleyois.boix-chova@axians.com
Patrik Sohlman
patrik.sohlman@axians.com

## Slide 2: Day 2
Day 1 Recap
Create IoT Hub and mSB Organization
Integrate Cisco Jasper
Provisioning new gateways
IoT Message Exchange Patterns
Common IoT protocols (skapa slides)
Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 3
“Any PROTOCOL”
“Any DEvice”
“Any Data Source”
“Any IoT platform”
Challenges
  Onboarding
  Hub independence
  Updates & Patches
  Issue tracking
  Monitoring
Monitoring
Machine
Learning
Reports
Apps
LOB
Modbus
Wi-Fi
LoRa
Serial
DATA
Value
DATA
PROTOCOL

## Slide 4
Business Solution
Gateway (Devices)
Communi-cation
Cloud
IoT Operations
IoT Operations generic offering
PLC’s
Machines, Sensors,
meters etc...
Set price per device & month.
IoT Nordic

## Slide 5: Axians – IoT Operation
Device Mgmt
IOT HUB
Customer B
IOT HUB
Customer C
IOT HUB
Customer A

## Slide 6: Axians – IoT Operation
SERVICE DESK
NETWORK OPERATIONS CENTER
Device Mgmt
IOT HUB
Customer B
IOT HUB
Customer C
IOT HUB
Customer A

## Slide 7: Axians – IoT Operation
Device Mgmt
IOT HUB
Customer B
IOT HUB
Customer C
IOT HUB
Customer A
Incidents
Issue tracking
Problem Management
Change Management
Release Management
Knowledge base
ITIL
SERVICE DESK
NETWORK OPERATIONS CENTER

## Slide 8: IoT platforms
Transport
REPORTS
SQL / NOSQL
ERP / LOB
GATEWAY/ DEVICE
Sensor
Data
RULES & ROUTING
SECURITY
DEVICE MGMT
API
API
Node.js
ARM mbed
Java
.Net
Python
MQTT
AMQP
WebSockets
HTTP
Certificates
SAS
Revoke
Add/Remove
Enable/Disable
Metadata
State

## Slide 9: microServiceBus Architecture (node.js)
Field Gateway
Operating system
Linux
Platform
Node.js
Agent
microServiceBus-node
Service
Service
Service
Agent
microServiceBus-core
Responsible for communication with mSB.com
Rarely updates (once or twice a year)
Interacting with sensors & business logic
Frequently updates (weekly)
Responsible for IoT Hub & orchestration of services
Often updates (once or twice a month)

## Slide 10: microServiceBus.com and related projects are property of Vinci-Energies!

## Slide 11: What is Node.js?
Node.js® is a JavaScript runtime built on Chrome's V8 JavaScript engine.
Node.js uses an single threaded, event-driven, non-blocking I/O model that makes it lightweight and efficient.
Node.js is platform independent.

## Slide 12: What is JavaScript?
A high-level, dynamic, untyped, and interpreted programming language. It has been standardized in the ECMAScript language specification
Notes: High-level … förlåtande
Förklara att javascript är ett JIT kompilerat språk
var a = 2;
console.log(a);
3();

## Slide 13: Node Package Manager (NPM)
npm is the default package manager for the JavaScript runtime environment Node.js and allows users to consume and distribute JavaScript modules that are available on the registry.
Npm has over 500K+ packages today, which is almost as much as Java, .Net and Python combined!

## Slide 14: microServiceBus.com - Key concepts
Organization
Nodes
Flows
Services
Code interacting with HW or other services
Inbound service
Outbound service
Other service
Process execution of services
Cloud connected agent, hosting one or more flows
“Subscription” owning flows, services & nodes

## Slide 15: Day 2
Day 1 Recap
Create IoT Hub and mSB Organization
Integrate Cisco Jasper
Provisioning new gateways
IoT Message Exchange Patterns
Common IoT protocols
Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 16: Lab #1 Create IoT Hub and mSB Organization

## Slide 17: Day 2
Day 1 Recap
Create IoT Hub and mSB Organization
Integrate Cisco Jasper
Provisioning new gateways
IoT Message Exchange Patterns
Common IoT protocols
Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 18: On-boarding
IoT Hub
microServiceBus.com
IOT HUB
DEVICE MANAGEMENT
SIM CARD MANAGEMENT
1. Activate SIM card
2. Request config
3. Notification
4. Register device
5. Credentials
6. Config
IOT DEVICE
7. Send & Receive
?

## Slide 19: Lab #1 Integrate Cisco Jasper
Instance: https://restapi3.jasper.com/rws/api/v1
User name: TUTORIALAPI
REST API key: 52098541-a1ed-4a33-84a2-13fbbf5723e2
Shared secret: Ignore
Trainer email: aleyois.boix-chova@axians.com

## Slide 20: Day 2
Day 1 Recap
Create IoT Hub and mSB Organization
Integrate Cisco Jasper
Provisioning new gateways
IoT Message Exchange Patterns
Common IoT protocols
Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 21: Lab #1 Provisioning new gateways

## Slide 22: Day 2
Day 1 Recap
Create IoT Hub and mSB Organization
Integrate Cisco Jasper
Provisioning new gateways
IoT Message Exchange Patterns
Common IoT protocols
Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 23: IoT Message Exchange Patterns
Events
Massive stream of information. Managed outside the IoT Hub
Messaging
C2D communication using a pub/sub pattern using topics & subscriptions
Methods
Devices exposes methods that can called from a external applications using a request/response pattern
State
Device state is exchanged using device-twin configuration stored in the IoT Hub.

## Slide 24: IoT Message Exchange Patterns
Stream Analytics
Cosmo DB
Machine Learning
Events
Function App
Logic App
Custom
Messaging
IoT Hub
Devices

## Slide 25: IoT Message Exchange Patterns
State
IoT Hub
Devices
Tags
Desired
Reported
Function App
Logic App
Custom
Twin

## Slide 26: Day 2
Day 1 Recap
Create IoT Hub and mSB Organization
Integrate Cisco Jasper
Provisioning new gateways
IoT Message Exchange Patterns
Common IoT protocols
Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 27: Common IoT protocols

## Slide 28: Common IoT protocols
De facto standard communication protocol, widely spread for connecting industrial electronic devices.
Devices: Heat pumps, energy meters, PLC, …
Other versions: Modbus RTU, Modbus TCP, …

## Slide 29: Modbus

## Slide 30: Common IoT protocols
M-bus (Meter-Bus) standardized protocol for remote reading of meters.
Other versions: Wireless M-bus.

## Slide 31: Wireless M-Bus
31 44 b0 5c 82 86 00 00 02 1b 7a fb 00 00 00 2f 2f 0a 66 34 02 0a fb 1a 45 02 02 fd 97 1d 00 00 2f 2f 2f 2f 2f 2f 2f 2f 2f 2f 2f 2f 2f 2f 2f 41 f8 9b
Header
Body

## Slide 32: Wireless M-Bus - Header
31 44 b0 5c 82 86 00 00 02 1b 7a
Manufacturer
Sensor Id
Type
Version
Length
Device Id
000086825cb0021b

## Slide 33: Wireless M-Bus

## Slide 34: Day 2
Day 1 Recap
Create IoT Hub and mSB Organization
Integrate Cisco Jasper
Provisioning new gateways
IoT Message Exchange Patterns
Common IoT protocols
Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 35: Getting Started
Gateway
Azure
Event Hub
Time Series Insight
microServiceBus.com
Azure
IoT Hub
Sensor

## Slide 36: Build a real world sensor to cloud solution
  Lab
    1. Receive whitelist through state
    2. Read telegrams from sensors and send to cloud
    3. Create Azure Event Hub and Time Series Insight

## Slide 37: Patterns and best practices
Gateways
Business applications
Event Hubs
Functions
Event Hubs
Functions
Data
IoT Hubs
Event Hubs
Event Hubs
Functions
Functions
Data
Data
IoT Hubs
Scenario 1
Scenario 2
Organization
Organization